## Slide 1
Quantum Communications Group
Supervisors:
Armando Nolasco Pinto
anp@ua.pt
Diogo Matos
dftm@ua.pt
Key Management System for a QKD Network
Weekly Report

## Slide 2: General Architecture

## Slide 3: KMS interface to the apps – ETSI 004 (pull mode)
The interaction between the KMS and the app relies on three requests:
OPEN_CONNECT(in source, in destination, in QoS, inout Key_stream_ID, out status)
Is made by an app to create a key stream with the characteristics specified in the QoS field. A Key Stream Id (KSID) and a status value are returned. If the OPEN_CONNECT request is made with a value in the Key_stream_ID field, it connects to an existing Key Stream instead of creating a new one.
GET_KEY(in Key_stream_ID, inout index, out Key_buffer, inout Metadata, out status)
Is used by the apps to retrieve keys. It can be made with or without an index. With a given index, the KMS will return the key, if exists, with that index. Otherwise, it returns the oldest key that was created by its peer but not retrieved yet, if there is no keys to be return, a new one will be created and returned alongside with its index.
CLOSE(in Key_stream_ID, out status)
Is used to terminate a Key Stream connection. The peer still can retrieve already created and unexpired keys.

## Slide 4: KMS interface to the physical layer – ETSI 004 (push mode)
  The KMS is always receiving keys without making individual requests for each one. The interface between the KMS and the physical layer is basically the same as the one provided by the KMS for the applications to use but now the KMS will act like an application requesting key material.
  The KMS will start by making an OPEN_CONNECT request to create a connection to the physical layer. Then does one GET_KEY request and from that moment forward it will receive key material with the characteristics and pace specified in the QoS field until it makes a CLOSE request to terminate the key stream.

## Slide 5: QOS parameters
Key_type: key type for the key stream (not approved yet).
Key_chunk_size: Length of the key buffer requested by the application (uint32_t).
Max_bps: Maximum key rate requested in bits per second (uint32_t).
Min_bps: Minimum key rate requested in bits per second (uint32_t).
Jitter: Maximum expected deviation, in bps, for key delivery (uint32_t).
Timeout: Time, in msec, after which the all will be aborted, returning an error.
TTL: Time after which the keys corresponding to this Key_stream_ID shall be erased(uint32_t).
Metadata mimetype: Field that defines the format of the metadata on each subsequent GET_KEY call.

## Slide 6: Messages Exchanged