## Slide 1
Quantum Communications Group
Group Coordinator:
Group Websites:
Armando Nolasco Pinto
anp@ua.pt
https://www.it.pt/Groups/Index/72
LinkedIn: https://www.linkedin.com/company/quantum-communications-group-it-av/
Key provisioning interface
Diogo Matos

## Slide 3: OPEN
APP → KMS : Src, Dst, QoS, [INDEX]
APP ← KMS : KSID, QoS, STATUS
QoS fields:
  Key_type - 0: classical symmetrical, 1: P.Q. symmetrical, 2: quantum symmetrical, 3/4: classical oblivious (A/X), 5/6: P.Q. oblivious (A/X), 7/8: quantum oblivious (A/X).
  Key_chunck_size - length of the key buffer, in Bytes, requested by the app.
  Max_bps - Maximum key rate, in bps, requested by the app.
  Min_bps - Minimum key rate, in bps, requested by the app.
  Jitter - Maximum expected deviation for key delivery.
  Priority - Priority of the request (to be defined).
  Timeout - time, msec, after which the call will be aborted, returning an error.
  Time to live - Time, in seconds, after which the keys for this KSID shall be erased from the application’s dedicated key store.
  Metadata mimetype - The mimetype (“application/json”, for example) of the metadata to be delivered by the KM on each GET call.
Notes: ReservA uma associação (Key_stream_ID) para um conjunto de chaves futuras em ambas as extremidades do link QKD através desta camada de gerenciamento de chaves QKD distribuída e estabelece um conjunto de parâmetros para definir os níveis esperados de qualidade de serviço. Esta função deve bloquear até que o peer seja conectado ou até que o valor Timeout no parâmetro QoS seja excedido.

## Slide 4: GET_KEY
APP → KMS : KSID, [INDEX]
APP ← KMS : KEY_BUFFER, METADATA, INDEX, STATUS
A key buffer has the following structure:
  { “key_buffer”: ……… ,
“metadata”: [ metadate_size (number of chars),
{ “KID”: …, “size”: … (bytes), “type”: …, “expires_at”: timestamp} ],
index,
status
}
Notes: Obter uma chave com as propriedades definidas anteriormente no QoS. A chave é retornada no key_buffer. Informação sobre a chave retornada é devolvida no campo de metadados, este campo é parcialmente dado no request, especificamente é indicado um determinado metadata_size (número de caracteres) que se for 0, faz com que os metadados não sejam devolvidos. Caso seja os metadados não couberem no dado tamanho, nenhuma chave deve ser devolvida, o status deverá refletir o problema ocorrido. O KMS tem a obrigação de sincronizar, autenticar e reservar chaves. O timeout desta para esta função é o indicado anteriormente no campo QoS do OPEN_CONNECT.

## Slide 5: CLOSE
APP → KMS : KSID
APP ← KMS : ACK, STATUS
Due to timing differences at the other end of the link this peer operation will happen at some other time and any unused keys shall be held until that occurs and then discarded or the TTL has expired
Notes: Termina a associação anexa ao dado KSID. Mais nenhuma chave deve ser alocada a este KSID. Contudo o peer pode continuar a pedir chaves que foram alocadas anteriormente até estas expirarem.

## Slide 6: Status code
0 → Successful
1 → Successful connection, but peer not connected (just a warning)
2 → GET_KEY failed because insufficient key available
3 → GET_KEY failed because peer application is not yet connected
4 → No QKD connection available
5 → OPEN failed because the KSID is invalid
6 → TIMEOUT
7 → OPEN failed, requested QoS cannot be met, counter proposal included
8 → OPEN failed, key type not supported yet
…